## Slide 1: Lightweight Face Detection on ARM Cortex-M7
Edoardo Mello Rella, Davide Menini

## Slide 2: Ideal Algorithm
Multi-Task CNN
  3 cascaded CNNs, for a total of 500k parameters
  Works with RGB images of any shape
  Various iterations at different scale
  Needs a quite high resolution to work properly
  Detects also face details (out of scope)
Accuracy
  86.55% with IoU-F1 metric
Great results, but definitely a dream for a MCU

## Slide 3: Real Implementation
Image Preprocessing on Host Device
  Gaussian smoothing to spread information over neighboring pixels accuracy
  Downscaling the max dimension to size 90 memory, accuracy
  Padding to size 90x60x3 using boundary values MCU constraint
  Normalization of intensities accuracy
Original CNN lightened and flashed on Cortex-M7 memory, accuracy
Postprocessing on Host Device
  CNN’s outputs transformed from predictions to boxes
  Clean-up to reduce false positives accuracy

## Slide 4: Real Implementation - CNN
Only 1st CNN (‘pnet’)
3 iterations at different input scale (, , 4) unrolled and concatenated
Single input and single output to be compliant with X-CUBE-AI validation process
Parameters | 19’896
RAM | 301 kB (205 kB + 96 kB)
ROM | 81 kB
MACs | 9’974’344
4

## Slide 5: Results - Accuracy
Accuracy: 76.62% with IoU-F1 metric (tolerance ±1)

## Slide 6: Results - Profiling
Profiling on STM32F756 @192MHz
Results from X-CUBE-AI (‘validate on target’), double checked by using the DWT_CYCCNT register to count cycles at runtime.
Duration (on average) | 363.6 ms
CPU cycles | 69’811’225
MACs | 9’974’344
Efficiency | 7 cycles/MAC (float32)
Bottleneck | 159 ms for 3rd conv2D

## Slide 7: Notes & Future Work
7 cycle/MAC is not optimal. We could accelerate it using some advanced DSP extensions of Cortex-M7 (e.g. CMSIS-DSP library)
Training the network by ourselves would allow some improvements:
  Higher accuracy
  Using grayscale images to reduce memory occupation and computation time
  Using float16 instead of float32
Postprocessing in C was complicate and would have required more time

## Slide 8
Thank you for your attention!